## Slide 1
IMS Gearbox Dash
Raspberry Pi Software Build — Status Update
Target: Raspberry Pi 5 + ILI9341 SPI LCD + GPIO Buttons + Actuators
Status:
Software complete & tested in mock mode — awaiting physical hardware test
EPICS Gearbox Project

## Slide 2
What We Built
A complete Raspberry Pi-targeted codebase that runs in mock mode on any PC
main.py
Entry point — boot state machine, event loop, coordinates everything
config.py
All GPIO pins, timings, constants, MOCK_HARDWARE flag
ui_dash.py
All drawing code extracted from the PC prototype — pixel-identical
input_gpio.py
Debounced button reader — Engine Start, Upshift, Downshift
actuators.py
H-bridge actuator control + gear shift state machine (threaded)
display_ili9341.py
SPI display driver — ILI9341 in landscape via MADCTL rotation
mock_hw.py
Mock GPIO/SPI — lets everything run on PC without hardware
requirements.txt
Python dependencies for PC and Pi
All files live under src/ — the original dash_f4_style.py is preserved as-is for reference
2

## Slide 3
How It Works
1
BLANK
Screen is black. Waiting for visitor to press Engine Start button.
2
LOGO
IMS logo fades in over 800 ms, stays visible for 5 seconds total. Splash/boot screen.
3
DASH
F4-style dashboard appears: gear, speed, RPM, fuel, water temp, lap timer. Visitor can now shift.
Shifting & Speed
Gears 1-4 only. Speed = 100 kph * (gear_ratio / 1st_ratio). Gives 100 / 129 / 157 / 187 kph. Lap timer counts up, resets at 1:25.500. Last lap is always 1:25.500.
3

## Slide 4
Key Design Decisions
MOCK_HARDWARE Flag
Environment variable toggles between PC mock mode (default) and real Pi hardware. Same code paths run in both — only the GPIO/SPI layer swaps out.
Actuator Safety
Never drives both H-bridge pins HIGH simultaneously (prevents shoot-through). All direction changes go through STOP first. Emergency stop function kills both actuators instantly.
Threaded Gear Shifts
Actuator movements run in a background thread so the UI never freezes during a shift. A lock prevents overlapping shift commands.
Sensor-Ready Architecture
Actuator positioning uses a PositionProvider interface. Currently time-based (no sensors). When limit switches or pots are added, swap in a new provider — zero UI changes.
Display Rotation via MADCTL
The ILI9341 panel is 240x320 portrait. Instead of rotating pixels in software, we set the MADCTL register to landscape mode — the display handles rotation in hardware.
Pixel-Identical UI
Drawing code extracted directly from dash_f4_style.py. Layout, colors, panel rendering, timing rules — all preserved exactly. No simplifications or changes.
4

## Slide 5
Actuator Control — Gear Mapping
Two actuators act as two 'rails' — each has extend / mid / retract positions
Gear
Actuator A
Actuator B
Speed
1st
Retract
Mid (neutral)
100 kph
2nd
Extend
Mid (neutral)
129 kph
3rd
Mid (neutral)
Retract
157 kph
4th
Mid (neutral)
Extend
187 kph
Safety Rules
Never drive IN1 + IN2 HIGH at the same time (prevents H-bridge shoot-through)
All transitions pass through STOP before changing direction
Emergency stop placeholder built in — kills both actuators instantly
5

## Slide 6
Issue: We Need an H-Bridge
Why We Can't Skip This
Voltage mismatch — Pi GPIO outputs 3.3V, actuators need 12V. GPIO pins physically cannot power them.
Current limit — GPIO pins source ~16 mA max. Actuators draw hundreds of mA under load.
Polarity reversal — the FA-MU-8-12-2 actuators change direction by swapping +/- wires. That's exactly what an H-bridge does.
What Does an H-Bridge Do?
An H-bridge is a circuit that lets you reverse the polarity of voltage to a motor/actuator using low-power control signals. It takes 3.3V logic inputs from the Pi and switches 12V power to the actuators in either direction.
Recommendation
L298N Dual H-Bridge Module
~$3–6 on Amazon
Handles 2 motors, accepts 12V input, works with 3.3V Pi logic. One module covers both actuators.
Budget Gap
The wiring diagram and software both assume H-bridges, but no H-bridge module was included in the parts budget. We need to order one L298N module (~$3-6) before physical testing can begin.
6

## Slide 7
How to Operate
PC Mock Mode (now)
Install:
pip install -r requirements.txt
Run:
python -m src.main
Controls:
ENTER = Engine Start
UP / W = Upshift
DOWN / S = Downshift
ESC = Quit
Actuator commands logged to console.
Raspberry Pi Mode (future)
Install:
pip install pygame RPi.GPIO spidev
Run:
MOCK_HARDWARE=0 python -m src.main
Hardware controls:
Engine Start = GPIO5 button
Upshift paddle = GPIO6 button
Downshift paddle = GPIO13 button
Requires wired LCD, buttons, H-bridge,
and actuators.
Not yet physically tested on hardware — mock mode has been verified on PC. Pi deployment pending H-bridge order + physical wiring.
7

## Slide 8
Next Steps
1
Order L298N H-Bridge
~$3-6 on Amazon. One dual module covers both actuators.
2
Wire Physical Setup
Connect LCD, buttons, H-bridge, and actuators to Pi per wiring diagram.
3
Deploy & Test on Pi
Run MOCK_HARDWARE=0 python -m src.main with real hardware connected.
4
Tune Actuator Timing
Adjust ACTUATOR_FULL_TRAVEL_MS and MID_TRAVEL_MS in config.py to match real stroke times.
8